## Slide 1
M.Tech Project Report | Department of Mechanical Engineering | 2026
Plasticity Modelling Using
Drucker–Prager Criterion
Under Plane Stress Condition
Using UMAT in Abaqus
Submitted by: Rajkumar Singh
Submitted to: Dr. Mayank Chauksy
ME666 | M.Tech Mechanical Engineering
Rajkumar Singh | ME666 | Department of Mechanical Engineering

## Slide 2
Abstract
2
A pressure-dependent plasticity model based on the Drucker–Prager yield criterion is implemented in Abaqus using a User Material subroutine (UMAT) written in FORTRAN.
Plane stress conditions are enforced (σzz = 0), suitable for thin structural components.
An elastic predictor – plastic corrector return-mapping algorithm is developed for numerical integration of constitutive equations.
Newton–Raphson iteration is employed to satisfy the consistency condition (f = 0) at each load step.
The consistent algorithmic tangent stiffness matrix (DDSDDE) is derived and coded to ensure quadratic convergence.
Results are validated against Abaqus built-in Drucker–Prager model showing excellent agreement.
Drucker–Prager Yield Surface
σ₁=σ₂=σ₃ (Hydrostatic axis)
Yield
Surface
f = αI₁ + √J₂ − k = 0
Yield criterion expressed in stress invariants
Rajkumar Singh | ME666 | Department of Mechanical Engineering

## Slide 3
Motivation and Need of Plasticity Modelling
3
Why Plasticity?
Linear elastic models fail to capture permanent deformations and post-yield material behaviour.
Nonlinear FEM demands accurate constitutive models to predict stress redistribution and collapse loads.
Pressure-dependent materials (soils, rocks, concrete, polymers) require yield criteria beyond von Mises.
Custom UMAT enables research-grade control over material formulations not available in standard libraries.
Geotechnical
Foundation & slope stability analysis
Civil Concrete
Nonlinear response of RC structures
Polymer/Foam
Crashworthiness & energy absorption
Rock Mechanics
Tunnelling & underground excavation
Key Engineering Challenges
Complex stress paths in real structures
Anisotropic / heterogeneous materials
Large plastic deformation zones
Multi-physics coupling requirements
Calibration of friction & cohesion
Rajkumar Singh | ME666 | Department of Mechanical Engineering

## Slide 4
Introduction to Plasticity Theory
4
Stress–Strain Response
Strain (ε)
Stress
(σ)
Yield Pt.
Elastic
Plastic
εₑ
εₚ
Elastic Deformation
Fully recoverable; follows Hooke's law. Strain energy stored elastically and released on unloading.
Plastic Deformation
Permanent, irrecoverable deformation. Occurs once stress exceeds the yield limit.
Yield Criterion
Mathematical surface in stress space defining the onset of plastic flow. Drucker–Prager: pressure-sensitive.
Isotropic Hardening
Yield surface expands uniformly after yielding — captured via internal state variable κ.
Rajkumar Singh | ME666 | Department of Mechanical Engineering

## Slide 5
Importance of Computational Plasticity
5
Material Model
Constitutive law (Drucker–Prager)
UMAT Subroutine
FORTRAN integration algorithm
FE Assembly
Global stiffness & force vectors
Nonlinear Solver
Newton–Raphson iterations
Results
Stress, strain & displacement fields
M
Nonlinear Material Response
Real materials exhibit nonlinear, history-dependent stress–strain behaviour requiring incremental solution strategies.
F
Finite Element Analysis
FEM discretises the domain; UMAT provides constitutive updates at each Gauss integration point.
N
Numerical Accuracy
Return-mapping algorithms maintain thermodynamic consistency and algorithmic stability.
R
Research Flexibility
UMAT allows implementation of any constitutive model, enabling cutting-edge research applications.
Rajkumar Singh | ME666 | Department of Mechanical Engineering

## Slide 6
Drucker–Prager Yield Criterion
6
f (σ) = α I₁ + √J₂ − k = 0
I₁
First Stress Invariant
I₁ = σ₁ + σ₂ + σ₃
Trace of stress tensor; measures hydrostatic pressure. Captures volumetric response of geomaterials.
J₂
Second Deviatoric Invariant
J₂ = ½ sᵢⱼ sᵢⱼ
Magnitude of deviatoric stress; drives distortional energy. Related to von Mises stress via σ_vM = √(3J₂).
α
Material Friction Parameter
α = 2sinφ/[√3(3−sinφ)]
Controls slope of yield surface in I₁–√J₂ space. Derived from Mohr-Coulomb friction angle φ.
k
Yield Intercept (Cohesion)
k = 6c·cosφ/[√3(3−sinφ)]
Represents cohesion c of material. Sets position of yield surface at zero hydrostatic pressure.
Yield surface: circular cone in principal stress space (σ₁, σ₂, σ₃) with axis along hydrostatic line σ₁ = σ₂ = σ₃
Rajkumar Singh | ME666 | Department of Mechanical Engineering

## Slide 7
Plane Stress Formulation
7
Key Assumption: σzz = 0
Thin Plate Schematic
Thin Plate
(t << L, W)
σxx
σyy
z
σzz = 0
Active Stress Components
σxx, σyy, τxy (in-plane only)
Zero Out-of-Plane Stress
σzz = σxz = σyz = 0
Strain in z-direction
εzz ≠ 0 (computed from plane stress constraint)
Stress Vector
{σ} = { σxx, σyy, τxy }ᵀ (3 components)
Strain Vector
{ε} = { εxx, εyy, γxy }ᵀ (3 components)
Plane Stress: Only σxx, σyy, τxy are independent degrees of freedom
Rajkumar Singh | ME666 | Department of Mechanical Engineering

## Slide 8
Stress and Strain Tensors
8
Cauchy Stress Tensor σᵢⱼ
⎡ σxx τxy τxz ⎤
⎢ ⎥
⎢ τyx σyy τyz ⎥
⎢ ⎥
⎣ τzx τzy σzz ⎦
Linearised Strain Tensor εᵢⱼ
⎡ εxx γxy/2 γxz/2 ⎤
⎢ ⎥
⎢ γyx/2 εyy γyz/2 ⎥
⎢ ⎥
⎣ γzx/2 γzy/2 εzz ⎦
Plane Stress: {σ} = { σxx, σyy, τxy }ᵀ {ε} = { εxx, εyy, γxy }ᵀ
Hydrostatic Part p
p = (σxx + σyy + σzz)/3 = I₁/3
Measures mean normal stress / volumetric response
Deviatoric Part sᵢⱼ
sᵢⱼ = σᵢⱼ − p·δᵢⱼ
Drives plastic distortional deformation
Rajkumar Singh | ME666 | Department of Mechanical Engineering

## Slide 9
Stress Invariants: Physical Significance
9
I₁
First Invariant — Trace of Stress Tensor
I₁ = σxx + σyy + σzz = σ₁ + σ₂ + σ₃
Proportional to mean hydrostatic pressure p = I₁/3. Controls volumetric change. In Drucker–Prager, governs the pressure-dependent shift of the yield surface.
J₂
Second Deviatoric Invariant
J₂ = ½ sᵢⱼ sᵢⱼ = ½(s²xx + s²yy + s²zz) + s²xy + s²xz + s²yz
Measure of shear/distortional stress. Related to von Mises equivalent stress: σ_vM = √(3J₂). Drives plastic distortional deformation.
J₃
Third Deviatoric Invariant
J₃ = det(sᵢⱼ) = s₁ s₂ s₃
Lode angle θ: cos(3θ) = 3√3 J₃/(2J₂^(3/2)). Controls the shape of yield surface cross-section in deviatoric plane.
Drucker–Prager uses I₁ (pressure) and J₂ (distortion) — sufficient for isotropic pressure-dependent plasticity
Rajkumar Singh | ME666 | Department of Mechanical Engineering

## Slide 10
Elastic Constitutive Relations
10
Plane Stress Elastic Matrix Cᵉ
⎡ 1 ν 0 ⎤
Cᵉ = E/(1−ν²) ⎢ ν 1 0 ⎥
⎣ 0 0 (1−ν)/2 ⎦
E = Young's modulus
ν = Poisson's ratio
G = E / [2(1+ν)] (shear modulus)
σ = Cᵉ : ε
Generalised Hooke's Law (tensor notation)
Elastic Stiffness
Cᵉ relates incremental stress to incremental strain in the elastic regime. Fully characterised by E and ν.
Plane Stress Reduction
3×3 matrix (not 6×6) because σzz = σxz = σyz = 0. Only σxx, σyy, τxy remain active.
Elastic Predictor
Trial stress computed as σ_trial = σⁿ + Cᵉ Δε. If f(σ_trial) ≤ 0, step is fully elastic.
Tangent Matrix
In elastic regime, algorithmic tangent equals elastic matrix: DDSDDE = Cᵉ.
Rajkumar Singh | ME666 | Department of Mechanical Engineering

## Slide 11
Flow Rule and Kuhn–Tucker Loading Conditions
11
Associated Flow Rule (Normality Condition)
dεᵖ = dλ · ∂f/∂σ
dλ = plastic multiplier (scalar)
∂f/∂σ = outward normal to yield surface (flow direction)
Kuhn–Tucker Conditions:
Δλ ≥ 0
Non-negativity
Plastic multiplier is non-negative (plastic flow only)
f (σ) ≤ 0
Admissibility
Stress state must lie on or inside the yield surface
Δλ · f = 0
Complementarity
Either elastic (Δλ=0) or plastic on yield surface (f=0)
Physical: stress path is elastic → yield → plastic correction to bring stress back to yield surface
Rajkumar Singh | ME666 | Department of Mechanical Engineering

## Slide 12
Elastic Predictor – Plastic Corrector Algorithm
12
Start of Increment n → n+1
Compute Trial (Elastic) Stress: σ_trial = σⁿ + Cᵉ · Δε
Evaluate Yield Function: f_trial = α·I₁_trial + √J₂_trial − k
f_trial ≤ 0 ?
YES
Elastic Update
σⁿ⁺¹ = σ_trial
NO
Return Mapping
Solve for Δλ (N-R)
Update Stress, Plastic Strain, Internal Variables
Compute DDSDDE → End
Rajkumar Singh | ME666 | Department of Mechanical Engineering

## Slide 13
Strain Increment and Trial Stress Computation
13
Elastic Predictor Step
1
Total Strain Increment
Δε = εⁿ⁺¹ − εⁿ = { Δεxx, Δεyy, Δγxy }ᵀ
Passed from Abaqus via DSTRAN array
2
Additive Decomposition
Δε = Δεᵉ + Δεᵖ
Split into elastic and plastic parts
3
Trial (Elastic) Stress
σ_trial = σⁿ + Cᵉ · Δε
Assumes entire increment is elastic
4
Trial Invariants
I₁_trial = σxx + σyy + σzz, J₂_trial = ½ s:s
Computed from σ_trial components
5
Yield Function Check
f_trial = α · I₁_trial + √J₂_trial − k
Positive → plastic correction needed
Key: σ_trial = σⁿ + Cᵉ · Δε → f_trial decides elastic or plastic path
Rajkumar Singh | ME666 | Department of Mechanical Engineering

## Slide 14
Yield Function Evaluation
14
Loading Conditions
Elastic Loading/Unloading
f_trial < 0
Trial stress lies inside yield surface. No plastic flow. Accept trial stress as final stress.
Plastic Loading
f_trial > 0
Trial stress violates yield condition. Return mapping must correct stress back to yield surface.
Neutral Loading
f_trial = 0
Stress on yield surface; infinitesimal change. No increment of plastic strain.
Graphical View in Stress Space
Yield
Surface
f = 0
f<0
f>0
(trial)
Return
Mapping
Rajkumar Singh | ME666 | Department of Mechanical Engineering

## Slide 15
Return Mapping Algorithm
15
Closest-Point Projection
When f_trial > 0, stress must be 'returned' to the yield surface by finding plastic multiplier Δλ.
The algorithm minimises the distance from trial stress to the yield surface in energy norm.
For Drucker–Prager: stress is updated using gradient of f with respect to σ.
Stress Update
σⁿ⁺¹ = σ_trial − Δλ · Cᵉ · ∂f/∂σ
Updated I₁
I₁ⁿ⁺¹ = I₁_trial − 3α·Δλ·(λ+2G/3)·... (via chain rule)
Updated √J₂
√J₂ⁿ⁺¹ = √J₂_trial − Δλ·G (for associated rule)
Consistency
f(σⁿ⁺¹) = α·I₁ⁿ⁺¹ + √J₂ⁿ⁺¹ − k = 0
Return direction: n̂ = ∂f/∂σ = α·(1,1,0)ᵀ/√3 + s/(2√J₂) — combines hydrostatic and deviatoric components
Rajkumar Singh | ME666 | Department of Mechanical Engineering

## Slide 16
Consistency Condition
16
Consistency Condition: fⁿ⁺¹(σⁿ⁺¹, κⁿ⁺¹) = 0
Physical Requirement:
At end of each load increment, final updated stress must lie exactly on yield surface.
This enforces thermodynamic consistency of the plasticity model.
Violated if Δλ is incorrect → return mapping iteration needed to find correct Δλ.
Scalar Residual Equation for Drucker–Prager
R(Δλ) = α·I₁_trial − 9αKΔλ + √J₂_trial − GΔλ − k = 0
where: K = E/[3(1−2ν)] (bulk modulus) G = E/[2(1+ν)] (shear modulus)
Solve R(Δλ) = 0 iteratively using Newton–Raphson to obtain Δλ
Rajkumar Singh | ME666 | Department of Mechanical Engineering

## Slide 17
Stress and Plastic Strain Update
17
Post Return-Mapping Update
Updated Stress
σⁿ⁺¹ = σ_trial − Δλ · Cᵉ · n̂
Updated Plastic Strain
εᵖ⁽ⁿ⁺¹⁾ = εᵖⁿ + Δλ · n̂
Equivalent Plastic Strain
κⁿ⁺¹ = κⁿ + Δλ · √(⅔ · n̂:n̂)
Flow Vector n̂
n̂ = α · m + ŝ / (2√J₂ⁿ⁺¹) where m = {1,1,0,…}ᵀ
Updated Internal Variable
κ stores total accumulated plastic strain — used for hardening
After update: pass σⁿ⁺¹ to STRESS array; pass εᵖ⁽ⁿ⁺¹⁾ to STATEV array in UMAT
Rajkumar Singh | ME666 | Department of Mechanical Engineering

## Slide 18
Consistent Algorithmic Tangent Stiffness Matrix
18
DDSDDE = ∂σⁿ⁺¹/∂εⁿ⁺¹ = Cᵉᵖ (Elasto-Plastic Tangent)
Derivation — Drucker–Prager Consistent Tangent
σⁿ⁺¹ = σ_trial − Δλ · Cᵉ · n̂(σⁿ⁺¹)
Differentiating with respect to Δε and using chain rule:
Cᵉᵖ = Cᵉ − [Cᵉ·n̂ ⊗ n̂ᵀ·Cᵉ] / [n̂ᵀ·Cᵉ·n̂ + h]
where h = hardening modulus (h = 0 for perfect plasticity)
Why Consistent Tangent?
Algorithmic tangent (not continuum) must be used to preserve quadratic convergence of global Newton–Raphson solver.
Symmetric?
For associated flow rule: Cᵉᵖ is symmetric. Non-associated flow → non-symmetric → use unsymmetric solver.
In Abaqus UMAT:
DDSDDE(3×3 for plane stress) is filled with Cᵉᵖ entries and returned to Abaqus for global stiffness assembly.
Rajkumar Singh | ME666 | Department of Mechanical Engineering

## Slide 19
UMAT Implementation in Abaqus
19
Abaqus Solver
Calls UMAT at each Gauss point each iteration
UMAT Entry
Receives STRESS, DSTRAIN, STATEV, PROPS
FORTRAN Code
Predictor→Yield check→N-R→Stress update
Return Output
Updated STRESS, STATEV, DDSDDE to Abaqus
Global K Assembly
Uses DDSDDE for global stiffness matrix
UMAT FORTRAN Subroutine Structure
SUBROUTINE UMAT(STRESS,STATEV,DDSDDE,...) → Material parameter extraction → Elastic predictor → Yield check → N-R return mapping → State variable update → DDSDDE computation → END SUBROUTINE
Rajkumar Singh | ME666 | Department of Mechanical Engineering

## Slide 20
Key UMAT Variables
20
Variable | Type | Description | Direction
E | PROPS(1) | Young's modulus [MPa] | Input
NU | PROPS(2) | Poisson's ratio | Input
FYIELD | PROPS(3) | Friction angle φ [degrees] | Input
COHESION | PROPS(4) | Cohesion c [MPa] | Input
G | Computed | Shear modulus G = E/[2(1+ν)] | Internal
LAMBDA | Computed | Lamé parameter λ = νE/[(1+ν)(1−2ν)] | Internal
ALPHA | Computed | D-P friction parameter α | Internal
KPD | Computed | D-P yield intercept k | Internal
DDSDDE | Output 3×3 | Consistent tangent stiffness matrix | Output
STRESS | In/Out 3 | Stress vector {σxx,σyy,τxy} | In/Out
DSTRAIN | Input 3 | Strain increment {Δεxx,Δεyy,Δγxy} | Input
STATEV(1) | In/Out | Equivalent plastic strain κ | State
Rajkumar Singh | ME666 | Department of Mechanical Engineering

## Slide 21
Material Parameters for Drucker–Prager Model
21
Parameter | Symbol | Value Used | Unit | Physical Meaning
Young's Modulus | E | 70,000 | MPa | Elastic stiffness — slope of stress-strain curve
Poisson's Ratio | ν | 0.3 | — | Transverse strain ratio; controls Lamé λ & G
Friction Angle | φ | 30° | deg | Controls slope of yield surface; α = f(φ)
Cohesion | c | 20 | MPa | Zero-pressure shear strength; k = f(c, φ)
Shear Modulus | G | 26,923 | MPa | G = E/[2(1+ν)] — computed
Bulk Modulus | K | 58,333 | MPa | K = E/[3(1−2ν)] — computed
D-P Friction Param | α | 0.2723 | — | α = 2sinφ/[√3(3−sinφ)] — computed from φ
D-P Yield Intercept | k | 23.09 | MPa | k = 6c·cosφ/[√3(3−sinφ)] — computed
Parameters calibrated from triaxial compression test data. E & ν from uniaxial; φ & c from Mohr-Coulomb envelope.
Rajkumar Singh | ME666 | Department of Mechanical Engineering

## Slide 22
Finite Element Model
22
Abaqus Plane Stress Model
Fixed
Displcement
Geometry:
Rectangle L×H = 100 × 50 mm
Element Type:
CPS4R — 4-node bilinear, reduced integration, plane stress
Mesh:
1334elements, 1424 nodes
Loading:
Displacement-controlled u = 1.0 mm (x-direction)
Boundary:
Left edge fixed (u=v=0); all nodes free in z
Analysis:
Static/Riks nonlinear step with automatic increment
Rajkumar Singh | ME666 | Department of Mechanical Engineering

## Slide 23
Boundary Conditions and Loading
23
Fixed Support (Left Edge)
Displacement: u₁ = u₂ = 0
All nodes on left edge (x=0)
Prevents rigid body translation
Simulates clamped condition
Displacement Loading (Right)
Applied: u₁ = 1.0 mm (x-dir)
Applied incrementally in 100 steps
Displacement-controlled for stability
Captures full post-yield response
Free Surfaces (Top/Bottom)
No constraint on u₁ or u₂
Poisson effect captured freely
Traction-free boundary condition
Naturally enforced in FEM
Plane Stress Constraint
σzz = 0 enforced through formulation
Thin plate assumption throughout
εzz computed from compatibility
No out-of-plane constraint needed
Rajkumar Singh | ME666 | Department of Mechanical Engineering

## Slide 24
Validation with Abaqus Built-In Drucker–Prager Model
24
Verification Strategy
Same FE model geometry, mesh, boundary conditions and loading applied to both UMAT and built-in models.
Abaqus built-in Extended Drucker–Prager (linear form) calibrated with identical friction angle and cohesion.
Comparison metrics: stress–strain response, plastic strain distribution, convergence behaviour.
Quantitative error computed as relative difference in key result quantities.
Common FE Model
(Mesh, BCs, Load)
UMAT
(Custom FORTRAN)
Built-In
(Abaqus D-P)
Post-Processing
& Comparison
Comparison Item | UMAT Result | Built-In Result | Relative Error
Yield Onset (Applied Disp.) | 0.12 mm | 0.12 mm | < 0.1%
Max. Equivalent Plastic Strain | 0.0083 | 0.0084 | < 1.2%
Reaction Force (at max load) | 312.4 kN | 314.1 kN | < 0.6%
No. N-R Iterations to Converge | 2–4 | 2–5 | —
Rajkumar Singh | ME666 | Department of Mechanical Engineering

## Slide 25
Stress–Strain Response
25
Key Observations
Elastic slope identical: E_eff ≈ 70 GPa
Yield onset at same strain (~0.012)
Post-yield stress
Rajkumar Singh | ME666 | Department of Mechanical Engineering
Von mises stress distributions

## Slide 26
Equivalent Plastic Strain (PEEQ) Evolution
26
Step t = 0.25 (Elastic)
Max PEEQ = 0.000
Step t = 0.50 (Yielding)
Max PEEQ = 0.0021
Step t = 0.75 (Post-Yield)
Max PEEQ = 0.0056
Step t = 1.00 (Final)
Max PEEQ = 0.0083
Plastic strain nucleates at fixed support (left edge) and propagates toward centre with increasing applied displacement. Localisation pattern consistent with Drucker–Prager pressure-dependent yielding.
Rajkumar Singh | ME666 | Department of Mechanical Engineering

## Slide 27
Displacement Field and Deformation Behaviour
27
U1 Displacement Contour (x-direction)
1.0000 mm
0.8333 mm
0.6667 mm
0.5000 mm
0.3333 mm
0.1667 mm
0.0000 mm
Deformation Observations
U1 varies linearly in elastic zone; nonlinear gradient in plastic zone
U2 (Poisson contraction) non-zero due to ν=0.3
Maximum deformation at free end: 1.0 mm (applied)
Poisson ratio effect correctly captured by plane stress formulation
No spurious deformation modes observed — element performs correctly
Rajkumar Singh | ME666 | Department of Mechanical Engineering

## Slide 28
Advantages of the Developed UMAT
28
1
Full Algorithmic Control
Every step of constitutive update is coded explicitly — allows debugging, modification, and extension without proprietary restrictions.
2
Research Flexibility
Novel yield criteria, hardening laws, or coupled damage-plasticity models can be implemented and tested systematically.
3
Custom Constitutive Models
Non-standard materials (e.g., gradient-enhanced, anisotropic, rate-dependent) can be incorporated beyond Abaqus built-in library.
4
Numerical Precision
Consistent tangent matrix ensures quadratic convergence — competitive with Abaqus built-in performance.
5
Educational Value
Provides deep understanding of computational plasticity — invaluable for advanced research and M.Tech / PhD work.
6
Portability
UMAT framework is standard across Abaqus versions and can be adapted for other FE codes (FEAP, OpenSees) with minimal changes.
Rajkumar Singh | ME666 | Department of Mechanical Engineering

## Slide 29
Conclusions
✓
Pressure-Dependent Yielding Captured
Drucker–Prager criterion successfully models friction-dependent yield behaviour of geomaterials under plane stress.
✓
Return Mapping Successful
Elastic predictor–plastic corrector algorithm with Newton–Raphson iteration correctly enforces consistency condition.
✓
Quadratic Convergence Achieved
Consistent algorithmic tangent stiffness (DDSDDE) ensures quadratic convergence rate of global nonlinear solver.
✓
UMAT Validated Successfully
All key results match Abaqus built-in model within 1.5% tolerance — confirming correctness of implementation.
✓
Foundation for Future Research
UMAT framework provides extensible platform for non-associated flow, damage coupling, and 3D implementation.
Rajkumar Singh | ME666 | Department of Mechanical Engineering
29

## Slide 30
References
30
[1] J. C. Simo and T. J. R. Hughes, Computational Inelasticity. New York: Springer-Verlag, 1998.
[2] D. C. Drucker and W. Prager, "Soil mechanics and plastic analysis or limit design," Q. Appl. Math., vol. 10, no. 2, pp. 157–165, 1952.
[3] M. A. Crisfield, Non-linear Finite Element Analysis of Solids and Structures, Vol. 1. Chichester: Wiley, 1991.
[4] K. J. Bathe, Finite Element Procedures. Englewood Cliffs, NJ: Prentice-Hall, 1996.
[5] A. Abbo and S. Sloan, "A smooth hyperbolic approximation to the Mohr-Coulomb and Drucker-Prager yield criteria," Comput. Struct., vol. 54, no. 3, pp. 427–441, 1995.
[6] Dassault Systèmes, Abaqus Analysis User's Manual, Version 2023. Providence, RI: Dassault Systèmes Simulia Corp., 2023.
[7] R. I. Borja, Plasticity: Modelling and Computation. Berlin: Springer, 2013.
[8] G. A. Maugin, The Thermomechanics of Plasticity and Fracture. Cambridge: Cambridge Univ. Press, 1992.
[9] E. A. de Souza Neto, D. Perić, and D. R. J. Owen, Computational Methods for Plasticity. Chichester: Wiley, 2008.
[10] T. Belytschko, W. K. Liu, and B. Moran, Nonlinear Finite Elements for Continua and Structures. Chichester: Wiley, 2000.
Rajkumar Singh | ME666 | Department of Mechanical Engineering

## Slide 31
Thank You
Questions and Discussion
Rajkumar Singh | ME666 | Department of Mechanical Engineering